Modulation is a data transmission technique that transmits a message signal inside another higher frequency carrier by altering the carrier to look more like the message.
Quadrature amplitude modulation (QAM) is a modulation scheme that moderates two sinusoidal carriers 90 ° out-of-phase with each other. The components of each carrier are called inphase and quadrature. Both modulated carriers are summed to result in a signal with amplitude and phase modulation. The spectrum of the QAM signal is centered on the symbol rate frequency.
### Quadrature amplitude modulation can be used with a variety of different formats: 8QAM, 16QAM, 64QAM, 128QAM, 256QAM, but there are performance differences and trade-offs
QAM, quadrature amplitude modulation provides some significant benefits for data transmission. As 16QAM transitions to 64QAM, 64QAM to 256 QAM and so forth, higher data rates can be achieved, but at the cost of the noise margin.
Many data transmission systems migrate between the different orders of QAM, 16QAM, 32QAM, etc., dependent upon the link conditions. If there is a good margin, higher orders of QAM can be used to gain a faster data rate, but if the link deteriorates, lower orders are used to preserve the noise margin and ensure that a low bit error rate is preserved.
As the QAM order increases, so the distance between the different points on the constellation diagram decreases and there is a higher possibility of data errors being introduced. To utilise the high order QAM formats, the link must have a very good Eb/No (in digital communication or data transmission, Eb/N0 (energy per bit to noise power spectral density ratio) is a normalized signal-to-noise ratio (SNR) measure, also known as the "SNR per bit". It is especially useful when comparing the bit error rate (BER) performance of different digital modulation schemes without taking bandwidth into account. ) otherwise data errors will be present.When the Eb/No deteriorates, then other the power level must be increased, or the QAM order reduced if the bit error rate is to be preserved.
Accordingly there is a balance to be made between the data rate and QAM modulation order, power and the acceptable bit error rate. Whilst further error correction can be introduced to mitigate any deterioration in link quality, this will also decrease the data throughput.